## Slide 1
Investigating the Influences of Various Complexity of Hydrogeological Models on Pore Water Pressure Distribution Due to Seismic Wave Propagation
Name: Agustina Shinta Marginingsih
Advisor: Prof. Shih-Jung Wang
Date:2022/03/04

## Slide 2
Introduction
Methodology
Preliminary Result
Conclusions
Future Work
Outline
1

## Slide 3
Pore Water Pressure and Soil Liquefaction
Introduction
When the pore water pressure reaches the total stress the effective stress is lost. This mechanism can be stated by the principle of effective stress, introduced by Van Terzaghi (1936):
Full liquefaction occurs when the effective stress is equal to 0, where,
‘: Effective stresses
: Total stress
Pore-water pressures
Ground failure or loss of strength that causes otherwise solid soil to behave temporarily as a viscous liquid. The phenomenon occurs in water-saturated unconsolidated soils affected by seismic which cause ground vibrations during earthquakes.
Source: https://www.britannica.com/science/soil-liquefaction
2

## Slide 4
Seismic Wave Propagation in Soil Layer
(Huded et al, 2020)
Example 1:
(Taiebat et al, 2010)
Example 2:
The seismic waves propagate from bedrock are modified by the presence of layered soil. Recent studies have shown that the presence of a liquefiable soil layer can significantly reduce inertial load liquefaction of soil layer prevents the transmission of seismic waves (mainly shear waves) acting as shield protecting the above layers (base isolation effect) (Huded et al. 2020).
3

## Slide 5
UBC-Sand Model
Elastic Response
The UBC-SAND model is a simple elastoplastic stress/strain model for simulating the liquefaction phenomenon of sand
with a relative density less than 80%.
Where: = Elastic shear modulus
= Elastic shear modulus number
= Elastic bulk modulus number
= Exponent variable that relates the elastic shear modulus to the mean effective stress (elastic shear modulus index)
Assumed to be isotropic and specified by elastic shear modulus () and bulk modulus ():
4
= Reference pressure (atmospheric pressure)
= Effective confining pressure
= Maximum shear stress

## Slide 6
UBC-Sand Model
Plastic Response
Shear failure
Volumetric Compression
Pressure cut-off
Where:
= Plastic shear modulus
= Current shear stress
= Failure shear stress
= Failure ratio
5
The behavior is defined by three types of yield function:

## Slide 7
Study Area
Tainan City, Taiwan
Liquefaction occurs during :
JiaSian Earthquake (
on 4th March 2010 ( )
Meinong Earthquake (= )
on 6th February 2016 ( )
Liquefaction Point
Depth Acceleration Point
Surface Acceleration Point
6

## Slide 8
Identify the wave propagation in various hydrogeological models
Asses the dynamic distribution of displacement and pore water pressure
Discuss the liquefaction events based on the assessment result
Objectives

## Slide 9
Flow Chart:
Methodology
Synthetic Model
Homogeneous medium
Perfect layer system
Pinch-out aquifer system
Real Case Model
Study area: Hsin-Hwa, Tainan City, Taiwan
Hydrogeological layer system
Hydrogeological heterogeneous system
Boundary condition and parameter setting
Dynamic displacement and pore water pressure simulation
Asses the acceleration behavior and the distribution of displacement and pore water pressure
Comparison of the acceleration, displacement and pore water pressure between synthetic and real case model
Assess the soil liquefaction events
Task 1:
Task 2:

## Slide 10
Scenario 2. Perfect layer system
Model Set up
Soil Parameter
Simplified Synthetic
Hydrogeological Model
Boundary condition
Saturated Medium
Scenario 1. Homogeneous medium
Scenario 3. Pinch-out aquifer system
Dimension:
Depth: 30 m
Width : 80 m
Sand
Clay
(Lu et al. 2020)

## Slide 11
Soil Parameter
Simplified Synthetic
Hydrogeological Model
Boundary condition
Modulus of elasticity (E) | 877 kN/m2
Elastic shear modulus number () | 1,100
Elastic shear modulus index (ne) | 0.5
Plastic shear modulus number () | 310
Plastic shear modulus index (np) | 0.4
Poisson’s ratio | 0.02
Undrained Poisson’s ratio | 0.495
Unit weight () | 18 kN/m3
Unit weight () | 20 kN/m3
Cohesion (c) | 0 kPa
Peak friction angle ( | 33.8
Constant volume friction angle ( | 33
Earth pressure coefficient () | 1
Post liquefaction calibration | 0.6
Reference pressure () | 100 kN/m2
Failure ratio () | 0.9
Modulus of elasticity (E) | 877 kN/m2
 | 1,100
Elastic shear modulus index (ne) | 0.5
 | 310
Plastic shear modulus index (np) | 0.4
Poisson’s ratio | 0.02
Undrained Poisson’s ratio | 0.495
 | 18 kN/m3
 | 20 kN/m3
Cohesion (c) | 0 kPa
 | 33.8
 | 33
 | 1
Post liquefaction calibration | 0.6
 | 100 kN/m2
 | 0.9
(Huded et al. 2020)
Sand Layer:
Model Set up

## Slide 12
Soil Parameter
Simplified Synthetic
Hydrogeological Model
Boundary condition
Modulus of elasticity (E) | 8500 kN/m2
Poisson’s ratio | 0.2
Undrained Poisson’s ratio | 0.495
Unit weight () | 16 kN/m3
Unit weight () | 20 kN/m3
Cohesion (c) | 10 kN/m2
Frictional angle ( | 33.8
Dilatancy angle ( | 0
Earth pressure coefficient () | 1
Modulus of elasticity (E) | 8500 kN/m2
Poisson’s ratio | 0.2
Undrained Poisson’s ratio | 0.495
 | 16 kN/m3
 | 20 kN/m3
Cohesion (c) | 10 kN/m2
 | 33.8
 | 0
 | 1
(Huded et al. 2020)
Clay Layer:
Model Set up

## Slide 13
Soil Parameter
Simplified Synthetic
Hydrogeological Model
Input and Boundary Condition
Surface: Free to move in x and y directions (Traction-free boundary condition)
Sides:
Absorbent boundary to eliminate reflection wave at the sides
Bottom: Fixed (Roller Boundary)
Driving Seismic Wave
The wave simulation will use the sinusoidal (a max: 0.3 g) wave as input.
The sinusoidal wave will be generated horizontally at the bottom of the domain.
Model Set up

## Slide 14
Preliminary Result
Perfect Layer System
Homogeneous System
Pinch-Out Aquifer System
Acceleration Direction
Pore water pressure distribution
Excess Pore Water Pressure Ratio
Time (sec)
(Byrne et al. 2003)
Chart: 

## Slide 15
Acceleration Direction
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Horizontal Displacement
Chart: 
Time (sec)
Displacement(m)
(Bowen et al. 2015)
Preliminary Result

## Slide 16
Acceleration Direction
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Acceleration
Chart: 
Time (sec)
Acceleration (m/sec2 )
10
20
30
-4
-2
0
2
4
(Byrne et al. 2003)
Preliminary Result

## Slide 17
Acceleration Direction
Perfect Layer System
Homogeneous System
Pinch-Out Aquifer System
Pore water pressure distribution
Chart: 
Time (sec)
(Byrne et al. 2003)
Preliminary Result
Excess Pore Water Pressure Ratio

## Slide 18
Acceleration Direction
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Horizontal Displacement
Chart: 
Time (sec)
Displacement(m)
(Bowen et al. 2015)
Preliminary Result

## Slide 19
Acceleration Direction
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Acceleration
Chart: 
Time (sec)
Acceleration (m/sec2 )
10
20
30
-4
-2
0
2
4
(Byrne et al. 2003)
Preliminary Result

## Slide 20
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Acceleration Direction
Pore water pressure distribution
Chart: 
Time (sec)
(Byrne et al. 2003)
Preliminary Result
Excess Pore Water Pressure Ratio
Why the bottom sandy layer not liquefy?

## Slide 21
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Acceleration Direction
Horizontal Displacement
Chart: 
Chart: 
Chart: 
Chart: 
Time (sec)
Displacement(m)
Top Left
Bottom Left
Top Right
Bottom Right
(Bowen et al. 2015)
Preliminary Result

## Slide 22
Perfect Layer System
Pinch-Out Aquifer System
Homogeneous System
Acceleration Direction
Acceleration
Chart: 
Chart: 
Chart: 
Chart: 
Time (sec)
Acceleration (m/sec2 )
Top Left
Bottom Left
Top Right
Bottom Right
10
20
30
-4
-2
0
2
4
(Byrne et al. 2003)
Preliminary Result

## Slide 23: Conclusion
The behavior of pore water pressure, acceleration, and displacement shows in the model.
Pore water pressure increase gradually and stay in the maximum value after the liquefaction occurs (Pore water pressure ratio =1).
Acceleration different in the surface.
The horizontal displacement…

## Slide 24: Future work
Fixing the boundary effect
Generate the real seismic wave under the synthetic hydrogeological model
Simulate the real data

## Slide 25: Unstable Computation
Chart: 

## Slide 26: Thank You

## Slide 27
Contractive Response
The early stages of loading in a cycle : the excess pore pressure increase with the decrease of vertical effective stress and stiffness.
Dilative Response
As loading continues to larger stress ratios : the excess pore pressure decreases and the vertical effective stress and the soil stiffness increase.
Contractive Response
Upon and after reversal of shear stress increment, the excess pore pressure increase and vertical effective stress and soil stiffness decrease.
Dilative Response
As the absolute value of the stress ratio exceeds a certain level in the reverse loading. The excess pore pressure decreases and the vertical effective stress and the soil stiffness increase.
Contractive Response
The final stress-ratio increment reversal in the loading cycle. The excess pore pressure increase and vertical effective stress and soil stiffness decrease.
The typical mechanism of response observed in different elements during the shaking:
For looser samples (higher confining pressure) the contractive response is more pronounced.
For denser samples (lower confining pressure) the dilative response is more pronounced.

## Slide 29
UBC-Sand Model
Plastic Response
Shear failure
Volumetric Compression
Pressure cut-off
Where:
= the increment of friction angle
= Plastic shear modulus
= Current pressure
= the increment of plastic shear strain
= Plastic shear modulus number
= Current friction angle
= Peak friction angle
= Failure ratio
= Strain
= Post liquefaction factor
= Pressure
= Plastic bulk modulus number
= Plastic bulk modulus exponent
= Pressure cut-off
5

## Slide 30
In first year, the simplified synthetic hydrogeological simulations can be generated for seismic wave propagation in the poroelastic medium.
Expected Result
In the second year, generate real-case wave propagation simulations use two hydrogeological models of the layer system and heterogeneous system.
Determine the behavior of dynamic distribution displacement and pore water pressure in different scenarios
After compare the synthetical and the real case model we can asses the soil liquefaction potential.